## Slide 1
NOTE 1: The workflow described in this file does not work on Windows OS.
NOTE 2: My workflow is executed in Miniconda installed on Ubuntu 22.04.
NOTE 3: Products from HYP3 can only be used with MintPy.
HYP3-ISCE2 WORKFLOW

## Slide 2
After install miniconda, create hyp3-isce2 virtual environment, and activate the environment, please run the following command:
Please install and initially set up miniconda by your self
Install hyp3-isce2 (https://github.com/ASFHyP3/hyp3-isce2) following instructions below:
git clone https://github.com/ASFHyP3/hyp3-isce2.git
cd hyp3-isce2
conda env create -f environment.yml
conda activate hyp3-isce2
python -m pip install -e .
conda install -c conda-forge pandas matplotlib geopandas contextily pyyaml openpyxl xyzservices

## Slide 3
WORKFLOW OVERVIEW
Identify Sentinel-1 bursts
Polygon cover study area
Desired time span
These steps can be run idenpendently
Download bursts
Generating batch scripts
Run hyp3-isce2
Merged images can be processed with SNAP, or ISCE2
Output only used for MintPy
Step 1
Step 2
Step 3

## Slide 4
The final product is the batch scripts to run hyp3-isce2 like the instructions below
Single burst process
Multiple-burst
2 bursts on 2020/06/04, 2 burst on 2020/06/16

## Slide 5
For example, here is the batch script I prepared for my processing (S1A, descending) with 9 bursts
--looks  multilooking ratio (10 range : 2 azimuth)

## Slide 6
Here is the explanation for multilooking ratio from the main page of hyp3-isce2

## Slide 7
First, access https://search.asf.alaska.edu/#/

## Slide 8: Select study area
2 approaches
Using your own shapefile
Drawing polygon/box

## Slide 9
Using your own shapefile
Click Filters

## Slide 10
Using your own shapefile
Click Import File
geocoordinate system must be WGS84

## Slide 11
Using your own shapefile

## Slide 12
Using your own shapefile
Here is the output

## Slide 13
Drawing polygon/box
Click the icon
select Draw a Polygon or Draw a box

## Slide 14
Drawing polygon/box
Draw your own polygon that covers the study area

## Slide 15: From Study Area to Data

## Slide 16
click Dataset

## Slide 17
select S1 Bursts

## Slide 18
choose Start Date
choose End Date
Note: Select a pair so that the temporal distance < 13 days
Because we just need to identify what bursts cover our study area

## Slide 19
select IW
select polarization based on your purpose
start with ascending first, same process for descending
then click Search

## Slide 20
Here are the bursts covering the polygon

## Slide 21
We need to notice the Full Burst ID

## Slide 22
When we click the bursts along the IW1, we notice the pattern in Full Burst ID
In this case they are:
069_146200_IW1
069_146199_IW1
069_146198_IW1
…
069_146190_IW1
069 is the Path
146 is repeated

## Slide 23
Repeat with IW2
In this case they are:
069_146201_IW2
069_146200_IW1
069_146199_IW1
…
069_146193_IW1
Based on the patterns, we will design the script to download data suitable for study area

## Slide 24: An advantage when using S1 bursts instead of full SLC image

## Slide 25
Here is the information of SLC images covering my study area in Taiwan
I go back to data in year 2017 for demonstration
I select SLC images

## Slide 26
My study area is covered by 2 different SAR scenes, which make it challenging for processing
I select SLC images

## Slide 27
When using S1 bursts, the study area will be covered by appropriate bursts.
The bursts will be merged to generate a complete scene in hyp3-isce2 process

## Slide 28
Here is the interferogram generated by hyp3-isce2 using descending bursts

## Slide 29
Here is the interferogram generated by hyp3-isce2 using ascending bursts

## Slide 30: Before downloading data
We need a Python script to identify the Burst ID and Acquisition time range

## Slide 31
Here is a program to help users export a table of S1 bursts covering the study area within the desired time range
Users need to input parameters based on information they’ve got from https://search.asf.alaska.edu/#/

## Slide 32
Come back to this slide for demonstration
For my study area, I would like to select 5 bursts
069_146200_IW1
069_146199_IW1
069_146198_IW1
069_146197_IW1
069_146196_IW1
196
197
198
199
200

## Slide 33
Then input to the required parameters
Remember to input data in the right format

## Slide 34
python S1_burst_search.py --config <config_filename>.yaml
Run the following script in the command prompt
Note that I run the script in the virtual environment hyp3-isce2 which was guided to install here https://github.com/ASFHyP3/hyp3-isce2

## Slide 35
The output of the script includes an Excel file containing the bursts satisfying input parameters, and an image of burst coverages

## Slide 36
Here is the content of Excel file, including 5 bursts acquired on 2025-01-09, and 5 bursts acquired on 2025-01-21

## Slide 37
Until this step, we have NOT downloaded any image scenes. We only indentify all bursts which satisfy 2 conditions:
Cover the study area
Available for the desired time span
completed
WORKFLOW OVERVIEW
Identify Sentinel-1 bursts
Polygon cover study area
Desired time span
These steps can be run idenpendently
Download bursts
Generating batch scripts
Run hyp3-isce2
Merged images can be processed with SNAP, or ISCE2
Output only used for MintPy
Step 1
Step 2
Step 3

## Slide 38
After generating the Excel file from step 1, you can run either download_bursts.py or generate_batch_scripts.py
If you want to download all bursts, please run the following command:
python download_bursts.py –config <config_filename.yaml>
The program will download bursts and automatically merge them into one complete image.
Remember to input storage_dir, the program will not run without this parameter
If you want to use another Excel file which contains other burst research results, you can input the file path to specific_burst_file

## Slide 39
Then, we need to generate batch scripts to run hyp3-isce2, please input necessary parameters into the config file, then run generate_batch_scripts.py
python generate_batch_scripts.py --config <config_filename.yaml>
If you need to use other burst_search_file, you can input here
If you keep it blank, the program will search for the Excel file based on input parameters in SEARCH section
If your pairing method is “sbas”, you need to get the SBAS pair information from the ASF homepage, which will be shown in next slides.

## Slide 40
Come back to the https://search.asf.alaska.edu/#/ front page at the step Select S1 Bursts
Select a burst in your search results, then click SBAS

## Slide 41
Adjust perpendicular baseline threshold
Adjust temporal baseline threshold
Zoom in/out to see image connection
Add or remove pair by yourself
Number of pairs generated
Click Download when finish selection

## Slide 42
The custom selected pairs will be shown in dashed line
If you want to remove a pair, select to the dashed line, then choose Remove
After click Download, you will get the file asf-sbas-pairs.csv, you need to provide its filepath to the config file (.yaml)

## Slide 43
After running generate_batch_scripts.py, you will get these files

## Slide 44
WORKFLOW OVERVIEW
Identify Sentinel-1 bursts
Polygon cover study area
Desired time span
These steps can be run idenpendently
Download bursts
Generating batch scripts
Run hyp3-isce2
Merged images can be processed with SNAP, or ISCE2
Output only used for MintPy
Step 1
Step 2
Step 3
completed